## Slide 1: AI 芯片
ZOMI
计算的工作原理
— AI 芯片基础

## Slide 2
Talk Overview
AI 计算体系
  深度学习计算模式
  计算体系与矩阵运算
AI 芯片基础
  通用处理器 CPU
  从数据看 CPU 计算
  通用图形处理器 GPU
  AI专用处理器 NPU/TPU
  计算体系架构的黄金10年

## Slide 3
https://arxiv.org/abs/1807.07928
Operational intensity(ops/byte)
MAC/Cycle
Peak
Performance
Number of PEs (Theoretical Peak Performance)
Bandwidth(BW)
Bounded
Compute
Bounded
BW to PEs
MAC/data
Performance(ops/sec)
optimal

## Slide 4: 服务器的性能趋势

## Slide 5: GPU 性能趋势

## Slide 6: 计算机架构的新黄金时代
A New Golden Age for Computer Architecture: History, Challenges and Opportunities https://www.youtube.com/watch?v=kFT54hO1X8M

## Slide 7: 编译器的黄金时代
The Golden Age of Compiler Design in an Era of HW/SW Co-design
https://www.youtube.com/watch?v=4HgShra-KnY

## Slide 8: 超算中心的性能

## Slide 9: 训练 AI 大模型的时间

## Slide 10: 逻辑电路技术趋势预测

## Slide 11: 谁会在乎算力呢？
Flops

## Slide 15: 你真的在乎算力？
物理定律和硬件本身很大程度决定了我们对机器的编程方式
Flops

## Slide 16: 你真的在乎算力？
当我们对计算本身有更深入的了解时候，
才会慢慢看到本质的问题：我的数据在哪里？
Flops

## Slide 17: 读取数据与计算的计算换算
How many operations must I do on some data to make it worth the cost of loading it?
So for every number load from memory, Need to do 80 Operations on it to break even.
Required Compute Intensity = = 80
2000 GFLOPs FP64
200 GBytes / sec
= 25 Giga-FP64 / sec
(FP64 = 8 bytes)

## Slide 18: 计算密集型
 | AMD Rome 7742 | Intel Xeon 8280 | NVIDIA A100
Peak FP64 Giga Flops | 2,190 | 2,300 | 19,500
Memory B/W (GB/sec) | 131 | 204 | 1,555
Compute Intensity | 134 | 90 | 100

## Slide 19: ZOMI并不是很在乎算力
Flops

## Slide 20
https://arxiv.org/abs/1807.07928
Operational intensity(ops/byte)
MAC/Cycle
Peak
Performance
Number of PEs (Theoretical Peak Performance)
Bandwidth(BW)
Bounded
Compute
Bounded
BW to PEs
MAC/data
Performance(ops/sec)
optimal

## Slide 21: 内存、带宽、时延
更应该关注

## Slide 22: DAXPY 计算 DEMO
2FLOPs：multiply & add
2 Memory Loads: x[i] & y[i] (per element)
Single Operation: FMA(fused multiply-add)

## Slide 23: 光与电的传播速度
Speed of Light = 300,000,000 M/S
Computer Clock = 3,000,000,000 Hz
所以在一个时钟周期内光的传播速度为 100mm (~4 inches)

## Slide 24: 光与电的传播速度
Speed of Light = 300,000,000 M/S
Computer Clock = 3,000,000,000 Hz
Speed of Electricity = 60,000,000 M/S
所以在一个时钟周期电流的传播速度为 20mm (~0.8 inches)

## Slide 25: 光与电的传播速度
Speed of Light = 300,000,000 M/S
Computer Clock = 3,000,000,000 Hz
Speed of Electricity = 60,000,000 M/S

## Slide 26: 处理器内部

## Slide 27: DAXPY 计算 DEMO
Intel Exon 8280
11,659 bytes can be moved in 89 ns
AXY demo move 16 byes per 89 ns latency
Memory efficiency = 0.14%
Memory Bandwidth: 131 GB/sec
Memory latency: 89 ns
memory bus is idle 99.86% of the time

## Slide 28: 不同芯片产品的计算性能
 | AMD Rome 7742 | Intel Xeon 8280 | NVIDIA A100
Memory B/W(GB/sec) | 204 | 131 | 1555
DRAM Latency(ns) | 122 | 89 | 404
Peak bytes per latency | 24,888 | 11,659 | 628,220
Memory Efficiency | 0.064% | 0.14% | 0.0025%

## Slide 29: 引用
https://www.youtube.com/watch?v=3jHi8E5C-18
https://www.youtube.com/watch?v=-P28LKWTzrI
https://www.youtube.com/watch?v=3l10o0DYJXg

## Slide 30
Notes: 30