## Slide 1: AI 芯片
ZOMI
NVLink基础与发展
— GPU 细节

## Slide 2
Talk Overview
GPU 图形处理
  GPU 逻辑模块划分
  算法到 GPU 硬件
  GPU 的软件栈
  图形流水线基础
  流水线不可编译单元
  光线跟踪流水线
硬件基础
  GPU 工作原理
  GPU AI编程本质
英伟达 GPU 架构
  GPU基础概念
  从 Fermi 到 Volta 架构
  Turing 到 Hopper 架构
  Tensor Code 和 NVLink 详解

## Slide 3
Talk Overview
工作原理
  Tensor Core – 分布式训练
  Instruction Pipeline – 指令流水
  CUDA Thread – CUDA 线程执行

## Slide 6
分布式训练

## Slide 7: 人工智能发展与大规模分布式训练

## Slide 8: 深度学习迎来大模型（Foundation Models）
自监督学习方法，可以减少数据标注，降低训练研发成本
模型参数规模越大，有望进一步突破现有模型结构的精度局限
解决模型碎片化，提供预训练方案
e.g. 语言模型 GPT-3
  8 张 V100，训练时长 36 年
  512 张 V100，训练近 7 个月

## Slide 9: 混合并行
Narayanan, Deepak, et al. "Efficient large-scale language model training on gpu clusters using megatron-lm." Proceedings of the International Conference for High Performance Computing, Networking, Storage and Analysis. 2021.

## Slide 10: 分布式训练系统
计算图跨节点切分
*
Partition graph
Dispatch
partitions
*
*
*
Send
Recv
Server0
Server1
Server0
Server1

## Slide 11: 分布式训练系统
计算图跨节点同步数据（权重weights）信息
*
*
ops
ops
Server0
Server1
*
*
ops
ops
Server2
Server3
*
ops
Server4

## Slide 12: 通讯硬件
机器内通信
  共享内存
  PCIe
  NVLink（直连模式）
机器间通信
  TCP/IP网络
  RDMA网络（直连模式）

## Slide 13: 通讯硬件
机器内通信
  共享内存
  PCIe
  NVLink（直连模式）
机器间通信
  TCP/IP网络
  RDMA网络（直连模式）

## Slide 14: 通信软件：提供集合通信
MPI
  通用接口，可调用 Open-MPI, MVAPICH2, Intel MPI, etc.
NCCL / HCCL
  GPU通信优化，仅支持集中式通信

## Slide 15: 集合通信
一对多：Scatter / Broadcast；多对一：Gather / Reduce；多对多：All-Reduce / All-Gather

## Slide 16
NVLink & NVSwitch 发展

## Slide 17: Have a Look
https://images.nvidia.com/aem-dam/Solutions/gtcs22/nvlink/multinode_nvlink_final_HD.mp4

## Slide 19
 | Second Generation | Third Generation | Fourth Generation
NVLink bandwidth per GPU | 300GB/s | 600GB/s | 900GB/s
Maximum Number of Links per GPU | 6 | 12 | 18
Supported NVIDIA Architectures | NVIDIA Volta™ architecture | NVIDIA Ampere Architecture | NVIDIA Hopper™ Architecture

## Slide 22
 | First Generation | Second Generation | Third Generation
Number of GPUs with direct connection / node | Up to 8 | Up to 8 | Up to 8
NVSwitch GPU-to-GPU bandwidth | 300GB/s | 600GB/s | 900GB/s
Total aggregate bandwidth | 2.4TB/s | 4.8TB/s | 7.2TB/s
Supported NVIDIA architectures | NVIDIA Volta architecture | NVIDIA Ampere architecture | NVIDIA Hopper architecture

## Slide 23: Reference 引用&参考
https://www.youtube.com/watch?v=I4qd412w_A0
https://images.nvidia.com/aem-dam/Solutions/gtcs22/nvlink/multinode_nvlink_final_HD.mp4
https://www.youtube.com/watch?v=MY7jZGZw9vA
https://www.youtube.com/watch?v=vY61ExKhnfA

## Slide 24
Notes: 24